## Slide 1: Stopping the chain reaction in drainage
01 · Introduction and background
The problem
When one pipe fails, its water loads its neighbours, and the failure can spread.
The question
Does adding network structure to failure risk beat risk-only maintenance?
The scope
Synthetic networks, pipe failures only, a simplified flow model.
Aim: test whether graph theory can choose which pipes to protect when the reinforcement budget is limited.
Graph Theory research assignment · 1 / 6
Notes: Open with the chain reaction: one blocked pipe pushes water onto others, which can overload and fail. The question is how to spend a limited reinforcement budget. Scope is deliberately small.

## Slide 2: What exists, and what is missing
02 · Literature review
Cascade models
Gives
Overload-and-redistribute rule; attack and defence studies.
Misses
Generic networks; no reinforcement budget.
Graph theory for water
Gives
Critical pipes found from topology and checked against SWMM.
Misses
Mostly single failures; few intervention tests.
Risk-based maintenance
Gives
Pipes ranked by risk and cost under a budget.
Misses
Network structure is not used.
Gap: none of the reviewed studies compares risk-only with risk plus structure under equal budgets. This is not proof that none exists.
Graph Theory research assignment · 2 / 6
Notes: Cascade theory gives the mechanism, graph studies of drainage find critical pipes, risk-based maintenance gives the decision framing. Each misses one piece. Sources: Motter and Lai, Crucitti et al., Motter, Rajabi et al., Ulusoy et al., Hajibabaei et al., Berardi et al.

## Slide 3: Simulate cascades, test five strategies
03 · Methodology
1 Network
56-node gravity-fed graph, 86 to 88 pipes, 3 outlets; five random networks.
2 Cascade
A pipe fails when load exceeds capacity; water reroutes by surviving pipe size.
3 Strategies
Same budget: A risk, B risk plus betweenness, C random, D none, E load.
4 Evidence
100 test trials per cell, shared random failures, Wilcoxon with Holm.
Se = λ r̂e + (1 − λ) b̂e with λ* = 0.75 (tuning data); 4 rainfall levels × 3 budgets (5, 10, 20% of pipes).
Graph Theory research assignment · 3 / 6
Notes: Walk left to right. The score blends individual risk with betweenness from demand nodes to outlets. Every strategy gets the same budget, the same reinforcement effect and the same random failures. The model is a routing approximation, not a hydraulic simulator.

## Slide 4: Fewer cut-off areas, not fewer failed pipes
04 · Results
Failed pipes
0 of 12
cells with a significant gain over risk-only (−0.5% to +2.9%)
D
0.177
A
0.151
B
0.148
Mean failure rate, θ = 1.3, 10% budget
Unmet demand
11 of 12
cells with a significant gain (2.1% to 18.6%), none worse
D
0.347
A
0.301
B
0.273
Mean unmet demand, θ = 1.3, 10% budget
Graph-based and risk-only differ on water delivery, not on pipe survival.
Graph Theory research assignment · 4 / 6
Notes: Headline result. On failed pipes the graph rule is not significantly different from risk-only after correction. On unmet demand it wins in 11 of 12 cells. Grey is no intervention (D), blue is risk-only (A), orange is the proposed rule (B). Lower is better.

## Slide 5: When does the graph score help?
04 · Results
Rainfall
18.6% → 6.0%
Unmet-demand gain shrinks from θ = 0.7 to θ = 1.6 at a 10% budget.
Risk quality
+2.0% to +2.9%
Failed-pipe gain appears only with noisy or structure-linked risk; +0.9% (not significant) when risk is accurate.
Critical pipes
ρ = 0.42
Betweenness vs true single-pipe impact; load and risk near 0. Top-10% critical pipes found: B 20%, E 13%, A 7%.
Trial by trial at θ = 1.6, B beats A in 21% of trials, loses in 26% and ties in 53%.
Graph Theory research assignment · 5 / 6
Notes: Gains fade as rain intensifies because a few reinforced pipes cannot stop widespread overload. The structural score is most useful when risk estimates are poor. Betweenness is a moderate proxy for true criticality in this model.

## Slide 6: Structure protects delivery, risk protects pipes
05 · Discussion and conclusion
Why
Risk-only targets the random blockages behind failed pipes; the structural score targets pipes whose loss cuts off demand.
Limits
Synthetic networks, simplified routing, assumed parameters. The unmet-demand gain is partly built into the model. Not real flood prevention.
Next
Real network data, SWMM validation, junction and pump failures, direct optimisation of the pipe set.
Answer: partly. Risk plus structure did not cut failed pipes significantly, but it cut unmet demand in 11 of 12 cells.
Graph Theory research assignment · 6 / 6
Notes: Close with the answer to the research question: partly. Explain why the two metrics diverge, state the limits plainly, and end on validation with real data as the next step.